## Slide 1: Digital Business Technologies
Communication Infrastructure

## Slide 2: Overview of communication
Communication Basics
Internet communication

## Slide 3: Communication Basics
Sender
Receiver
Messages
Signal: (analog , digital)
Medium (wire, air, cable, optical fiber)
Limited capacity (bandwidth in bits/second)
distance
transmission errors
propagation speed: time until first bit is received
packets
Needs PROTOCOL

## Slide 4
Signal
Data....Digital Signals
Cat...
0011 0010
1110 0110
1011 1111
0
1
0
1
1
0
0
1
0
0
1
0
binary signaling
Notes: 4

## Slide 5: Medium
There are several kinds of communications links.
  Wire
    Twisted pairs
    Coaxial cables
    Fiber optics
  Wireless
    Microwave transmission
    Satellite transmission

## Slide 6: Medium
twisted pair:
light source
Notes: STP(Shielded Twisted Pair)
UTP(Unshielded Twisted Pair)

## Slide 7: twisted pair
Twisted-pair cable
  Contains pairs of insulated copper wires
  Outer insulating jacket covers wires
Communication specific properties
  Copper wires twisted to reduce EMI and RFI
  Length: up to 100 meters
  Transmission speed: up to 10 Gbps
RJ-45 plug-in connector attaches cable to device
  Less expensive and more flexible than T-connectors
Two kinds of twisted pair cable: shielded and unshielded (preferred)
Category 5: 100 Mbps, 1 Gbps Ethernet
Category 6: 10Gbps
Notes: Electromagnetic interference (EMI)
  Caused by magnetic force fields
  Generated by certain electrical devices
    Fans, electric motors, portable heaters, air-conditioners
Radio frequency interference (RFI)
  Caused by electrical devices emitting radio waves
    Radio and television stations, radio operators, cable TV
  Problem when frequency matches network signal

## Slide 8: Medium
coaxial cable:
Notes: STP(Shielded Twisted Pair)
UTP(Unshielded Twisted Pair)

## Slide 9: Medium
two concentric copper conductors
bidirectional
broadband:
  multiple channels on cable
  HFC
  1-2 Gbps in short distance
coaxial cable:

## Slide 10: Medium
Fiber optics:
light source
plastic jacket
glass or plastic
cladding
fiber core
TOTAL INTERNAL REFLECTION
Corning’s standard submarine cables can have up to 144 fibers in a single cable housing

## Slide 11: Medium
high-speed operation:
high-speed point-to-point transmission (e.g., 10’s-100’s Gbps transmission rate)
low error rate:
repeaters spaced far apart
immune to electromagnetic noise
  Long-haul systems - 600 km repeater spacing
  Ultra-long haul systems - 2000 km repeater spacing (forward error correction coding, fast external modulators)
  Metro systems - 100 km repeater spacing
Fiber optics:

## Slide 12: Advantages of optical systems
Enormous capacity: bandwidth of 37 THz!!
Low transmission loss
  Optical fiber loss can be as low as 0.2 dB/km. Compare to loss of coaxial cables: 10 … 300 dB/km !
Cables and equipment have small size and weight
  A large number of fibers fit easily into an optical cable
  Applications in special environments as in aircrafts, satellites, ships
Immunity to interference
  Nuclear power plants, hospitals, EMP (Electromagnetic pulse) resistive systems (installations for defense)
Electrical isolation
  electrical hazardous environments
  negligible crosstalk
Signal security
  banking, computer networks, military systems
Silica fibers have abundant raw material

## Slide 13: Submarine Cables in North East Asia
SOURCE: ALCATEL

## Slide 14: Submarine Cables in North East Asia

## Slide 15: Wireless Media

## Slide 16: Terrestrial Microwave Transmission
Land-based, line-of-sight transmission
Approximately 20-30 miles maximum between towers
Transmits data at hundreds of millions of bits per second
Popular with telephone companies and business to business transmissions
  270 msec end-end delay
  e.g. up to 360 Mbps channels

## Slide 17: Microwave, Satellite transmission

## Slide 18: Satellite Microwave Transmission
Notes: LEO (Low Earth Orbit) - 100 miles to 1000 miles
  Used for pagers, wireless e-mail, special mobile telephones, spying, videoconferencing
MEO (Middle Earth Orbit) - 1000 to 22,300 miles
  Used for GPS (global positioning systems) and government
GEO (Geosynchronous Orbit) - 22,300 miles
  Always over the same position on earth (usually over the equator)
  Used for weather, television, and government operations
HEO (Highly Elliptical Orbit)
  Used by the military for spying and by scientific organizations for photographing celestial bodies
  When satellite is far out into space, it takes photos
  When satellite is close to earth, it transmits data

## Slide 19: Cellular Telephone
Wireless telephone service
  Also called mobile telephone, cell phone, and PCS
  4G: ~ 600 Mbps (download), ~270 Mbps (upload)
  5G: ~20Gbps
To support multiple users in a metropolitan area (market), the market is broken into cells
Each cell has its own transmission tower and set of assignable channels
Notes: CTSO: cellular telephone switching office

## Slide 20: Cellular Telephone(x)

## Slide 21: Bluetooth
Radio Frequency specification for short-range, point-to-multipoint voice and data transfer
Can transmit through solid, non-metal objects
Its typical link range is from 10 cm to 10 m
  Can be extended to 100 m by increasing the power
Will enable users to connect to a wide range of computing and telecommunication devices without the need of connecting cables
Typical uses include phones and pagers, modems, LAN access devices, headsets, notebooks, desktop computers, and PDAs

## Slide 22: Bandwidth Review(x)
Bit (b) = a unit of information, 0 or 1
  10 bits can represent 1024 different messages
  20 bits represent > 1 million
  30 bits > 1 billion messages
The bandwidth of a communication channel = number of bits per second it transmits
All channels have limited bandwidth
One byte (B) = 8 bits (an octet)
Transmitting 1 MB at 56K bps takes 143 sec.
1 GB = gigabyte takes 40 hours
  at 7Mbps 19 minutes; at 1 Gbps takes 8 seconds)
Latency = delay from first bit transmitted to first received

## Slide 23: the simplest communication(x)
0/1
address / data
0: please send the data word at “address”
1: here is the data word you asked for.
header
payload
To transmit data between 2 computers
  Each computer has FIFO queue (buffer)
  Two way at the same time: full duplex
  bit stream with a fixed length: packet
  Packet format and rules : protocol
An example of hypothetical packet format and protocol

## Slide 24: Multipoint Communications
Addressing problem
  destination?
Impossible to connect each computer to all the others
  To connect n computers, need n(n-1)/2 links
  To connect 1 billion computers, need 5 x 1017 links
  Need switch equipments with one billion circuits
Connect all computers to one medium? No
  Capacity: too much traffic
  Collision: simultaneous messages interfere
  Vulnerability: pipe leaks, no one can talk

## Slide 25: Shared vs switched media
Shared media (e.g., Ethernet)
Switched media (e.g., ATM)
b
c
a
d
switch
a
c
b
d
a
c
b
d
b
c
a
d
switch
a
c
b
d
a
c
b
d
output ports
input ports
Notes: ATM: Asynchronous Transfer Mode,

## Slide 26: Circuit Switching v. Packet Switching
CIRCUIT-SWITCHED NETWORK
PACKET-SWITCHED NETWORK
A
B
Computer x
Computer y
B
A
B A
Message
Packet
Packet
Circuit switched network
  dedicated connection (circuit) between two nodes,
  held open for the entire exchange
  provides guaranteed capacity
  cost is independent of traffic
  E.g., Telephone system
Packet switched network
  transmissions divided into packets (data + metainfo)
  multiplexed onto high capacity intermachine connections
  allows multiple concurrent communication
  does not guarantee capacity
  E.g., the Internet

## Slide 27: Virtual Circuits
All commercial packet switched PSDNs use virtual circuits
  Eliminates forwarding decisions for individual packets
  Reduces switching load, so reduces switching costs
Virtual Circuit
Notes: PSDN: Packet Switched Data Network

## Slide 28: Network Topologies(x)
More than two computers causes complications:
Each machine on a network must have a unique address
If machine 2 sends a message to machine 4, what tells 1, 3 and 5 to ignore it, but 4 to listen?
Ethernet protocol
1
2
3
4
5
LAN BUS TOPOLOGY
LAN = LOCAL AREA NETWORK

## Slide 29: Network(x)
Two or more computers connected together:
Allows
  exchange of data
  separation of function (accounts receivable v. payroll)
  shared services (printers, databases)
  reliability
Requires
  interconnection (wire, fiber, infrared, radio)
  communication protocols

## Slide 30: The internetworking idea (Kahn, 1972)
Creation of an internet by interconnecting distinct constituent networks (internetwork, or internet)
  Each network exists already independently
  No need to change the existing network in order to connect to an internet
  Communicate by best-effort
  Use “black boxes” (called router later) to connect constituent networks
  None controls the whole network
One huge network that interconnects other networks
  Addressing (which node, which network?)
    Assigning a unique id to billions of nodes? (naming)
  Routing path (where to send a packet?)
    How to find each node? (forwarding and routing)
  Packets
    Arriving in wrong sequences (reorder packets)
    loss (have to be retransmitted)
    Include errors (correct or retransmit)
    Go through many nodes (time delay)
  advantages
    Even if one network is down, all the others are still working
    Interconnecting heterogeneous networks
  problems
    Provide transparency in a heterogeneous environment (Ethernet, FDDI, ATM, wireless)
    How to keep a standard?

## Slide 31: Structure of the Internet
Europe
Japan
Backbone 1
Backbone 2
Backbone 3
Backbone 4, 5, N
Australia
Regional A
Regional B
NAP
NAP
NAP
NAP
SOURCE: CISCO SYSTEMS
MAPS
UUNET MAP
KOREA
Notes: Network Access Point

## Slide 32: the Internet - network structure
Level 1 (interconnect level, NAPs)
Level 2 (national level, NSPs)
Level 3 (ISPs)
Level 4 (company, individual)
mobile network
global ISP
regional ISP
home
network
institutional
network
wired
links
wireless
links
router
smartphone
PC
server
wireless
laptop
Notes: NSP: Network Service Provider that owns backbone

## Slide 33: Internet characteristics
Open standard
  Transmission Control Protocol/Internet Protocol (TCP/IP)
    address
    sequence number
    message fragment
  packet-switched, wide-area network
  Separation of communication and Data processing
  Standard organization for internet technology
    IETF (Internet Engineering Task Force)
standard services: E-mail, file transfer, remote login, WWW
Transfer time
  Depends on bandwidth, traffic, message length
  Influenced by reordering message packets, retransmitting missing packets
Distributed control
  None controls the whole internet
  Each organization controls its own network
scalability
  Easy to connect and disconnect
  Easy to reconfigure sub-networks
Notes: 인터넷 관리
IETF(Internet Engineering Task Force): 표준 설정
IRTF(Internet Research Task Force)
IAB(Internet Architecture Board): IETF 감시, 분쟁조정
ISOC(Internet SOCiety): IETF funding, IAB 구성원 지명
IANA(Internet Assigned Number Authority)

## Slide 34: Protocol Stacks - TCP/IP versus OSI
OSI
  Subnet Layers
TCP/IP
  Upper layer above Subnet Layer
internet: Hybrid TCP/IP Architecture
OSI
Application (7)
Presentation (6)
Session (5)
Transport (4)
Network (3)
Data Link (2)
Physical (1)
TCP/IP
Application
Transport
Internet
Subnet
Data Link
Physical
internet
Application
Transport
Internet

## Slide 35: The TCP/IP Architecture and Protocol Suite

## Slide 36: Internet standard protocols
Application Layer (FTP, Telnet, WWW, email)
Transport Layer(TCP, UDP)
Internet Layer(IP)
Subnet
Standards
Data Link Layer(PPP, Ethernet)
Physical Layer
Application
Transport
Internet
Data Link
APDU
TPDU
IPDU
DLPDU
Application
Transport
Internet
Data Link
Physical
User PC
Server
PDU(protocol data unit)
Decompose Messages into
packets and assemble
Move packet to
the destination
thru the internet

## Slide 37
Notes: See pages 187 and 188 of Comer book

## Slide 38: Layer Cooperation
Ether-T
Adding Headers and Trailers:
Application
Transport
Internet
Data Link
HTTP msg
Physical
User PC
HTTP msg
TCP-H
HTTP msg
TCP-H
IP-H
HTTP msg
TCP-H
IP-H
Ether-H
packet
segment
Application
Transport
Internet
Data Link
Webserver
frame
on the Source Host
on the Destination Host
Removing Headers and Trailers:

## Slide 39: Internet Standards
ISP
ISP
Ethernet
PPP
App
Trans
Int
DL
Phy
User PC
Router
IP
PPP
Modem
Webserver
IP
Ether
?
HTTP
TCP
Int
DL
Phy
Int
App
Trans
Int
DL
Phy
DL
Phy

## Slide 40: HTTP (HyperText Transfer Protocol)
Sample HTTP Request
Browser
Webserver
Program
HTML
HTTP
User PC
Webserver
GET /report1/home.htm HTTP/1.1[CRLF]
Host:ddm.korea.ac.kr
Accept: image/gif.
Accept-Language: en
UA-pixels: 1024*768
UA-color: color16
UA-OS: Windows 98
Sample HTTP Response
HTTP/1.1 200 OK[CRLF] Date: Tuesday, 20-JAN-1999 18:32:15 GMT[CRLF] Server: name of server software[CRLF] MIME-version: 1.0[CRLF] Content-type: text/plain[CRLF] [CRLF] File to be downloaded.
Universal resource locator
[protocol]://[web server address]:[port]/[directory]/[file name]

## Slide 41: HTTP
HTTP with
  (a) multiple connections and sequential requests: http/1.1
  (b) A persistent connection and sequential requests.
  (c) A persistent connection and pipelined requests: http/2

## Slide 42: HTTP(x)
(a) Getting a Web page in HTTP/1.1
(b) Getting the same page in HTTP/2
HTTP/2
  Multiplexed Streams
  Stream Prioritization
  Server Push
  Header Compression

## Slide 43: TCP (Transmission Control Protocol)
Transport layer process stores the HTTP Request Temporarily
User PC transport process opens a connection to the webserver transport layer process
Next, user PC sends the HTTP Request
Transport layer process on the webserver receives the TCP segment delivering the HTTP Request
Webserver application creates the HTTP Response message
Webserver Transport Process Delivers the Response
Closing the Connection takes 4 TCP Segments

## Slide 44: TCP: Opens a Connection
Three Flags are Widely Used
  SYN bit set to 1 in a TCP segment to request a connection
  ACK bit set to 1 in a segment to acknowledge a received TCP segment
  FIN bit set to 1 in a segment to inform of a connection closure
User PC
Transport
Process
Webserver
Transport
Process
SYN
SYN, ACK
ACK

## Slide 45: TCP Segment Structure
Divided logically into sections called fields
  source port field is bits 0 to 15, …
Source Port # (16)
Destination Port # (16)
Sequence Number (32 bits)
Acknowledgement Number (32 bits)
Hdr Len
(4)
Flags (6)
Window Size (16)
Options (if any)
PAD
Bit 0
Bit 31
Reserved (6)
TCP Checksum (16)
Urgent Pointer (16)
TCP Segment
Data Field

## Slide 46: TCP: Request-Response
User PC
Transport
Process
Webserver
Transport
Process
TCP segment containing
HTTP Request
ACK
User PC
Transport
Process
Webserver
Transport
Process
TCP segment containing
HTTP Response
ACK

## Slide 47: TCP: Closing the Connection
User PC
Transport
Process
Webserver
Transport
Process
FIN
FIN
ACK
ACK

## Slide 48: TCP
ensures end-to-end delivery
fragment long application messages and transmits them in several TCP segments
implements flow control: send the next segment after receiving ack
TCP is reliable
  it does error correction
    Each TCP segment has a 32-bit sequence number that increases with each TCP segment a transport process sends
  it Places TCP Segments in Order
  protects against errors at lower layers as well as transport layer errors
    Retransmit if not receiving ack after sending a segment
high-overhead
  Executed only at the end nodes
  Multiple HTTP Request-Response Cycles can be Handled with a Single TCP Connection in HTTP/1.1 and later versions

## Slide 49: IP (Internet Protocol)
Connectionless Service
  No open, close, error correction, flow control
  Low overhead
  Unreliable
    No error handling
    No sequence numbers
IP Addresses and Router Forwarding

## Slide 50: Routing
Router A can send
the packet either way
Machine 1.35 wants to send a
packet to Machine 3.249.
Routers determine the path
the packet will take.
Routers
A
B
Machine
1.35
Machine
3.249
NETWORK 4 &
IT’S ROUTER
Machine
2.16
4.1
5.9
NUMBER OF ROUTES

## Slide 51: Routers
NORTEL
CISCO
3COM
SIEMENS

## Slide 52: IPv4 Packet Structure
Total datagram Length in bytes (16)
Time to Live (8)
Options (if any)
Bit 0
Bit 31
Version
(4)
Hdr Len
(4)
Type Of Service(8)
Identifier (16 bits)
Flags (3)
Fragment Offset (13)
Source IP Address
Destination IP Address
Header Checksum (16)
Upper layer
Protocol (8)
PAD
Data Field
“type” of data
for fragmentation/
reassembly

## Slide 53: IPv4 addresses
Prefixes: Network part
Subnets: Splitting an IP prefix into separate networks with subnetting
CIDR—Classless InterDomain Routing
Classful and special addressing
NAT—Network Address Translation

## Slide 54: IPv4 Internet addresses
IP addresses consist of network part + host part or network part + subnet part + host part
CIDR
0
1
2
8
16
24
network(7)
host (24)
0
31
network (14)
host (16)
1
0
network (21)
host (8)
1
1
0
Class A(128 nets, 16 M hosts/net)
Class B(16 K nets, 65 K hosts/net)
Class C (2 M nets, 256 hosts/net)
3 classes of addresses:

## Slide 55: NAT
NAT
  Home gateway/broadband router

## Slide 56: IPv6
Longer addresses than IPv4
Simplification of the header
Better support for options
Big advance is in security
Quality of service
Fixed Header
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
upper layer protocol or extension header
traffic class
2001:db8:3e8:100::1

## Slide 57: IPv6 Extension Headers
The hop-by-hop extension header for large datagrams
The extension header for routing

## Slide 58: Packet Switching (TCP/IP)
TCP = TRANSMISSION
CONTROL
PROTOCOL
(Breaks messages into packets
and reassembles them)
IP = INTERNET
PROTOCOL
(Moves packets around
the Internet)
SOURCE: J. DECEMBER

## Slide 59: Internet Standards - Data Link Layer
organize transmissions into collections of bits and manage their transmission within a single network
Concerned with exchange of data between an end system and the network
  sending computer provides destination address
  sending computer invokes services of network (e.g. priority)
  separates higher layers from details of network (e.g. X.25, Ethernet, Token Ring)
  only involves systems attached to same network
10010001001
Data Link
Frame

## Slide 60: Ethernet frame format
64 - 1518 bytes
Preamble
Dest
addr
Src
addr
Frame
type
Payload
CRC
Postamble
64 bits
48 bits
48 bits
16 bits
368-12000 bits
32 bits
8 bits
visible from the host
Preamble: 101010101 (synch)
Dest and Src addr: unique ethernet addresses
Frame type: indicates what packet type it encapsulates
  E.g. encapsulated IP packets are denoted by 0x0800
Payload: data (may include encapsulated packets of other protocols)
CRC: cyclic redundancy check (error detection/correction)

## Slide 61: Internet Standards - Physical Layer
Physical Layer Standards in Internet Access from Home
  connector plugs
    RJ11 Wall jack, Serial port, Model port
  transmission media
    Telephone wire, cable
  electrical signaling
    External modem
  Visible and tangible physical products: many suppliers can provide